## Slide 1: SIGCOMM’20 Tutorial Multipath Transport Protocols
Presenters
  Olivier Bonaventure, UCLouvain
  Quentin De Coninck, UCLouvain
Schedule
  10:00-11:00 EDT Multipath TCP, Olivier
  11:00-11:30 EDT Hands-on, Quentin
  12:00-13:00 EDT Multipath QUIC, Quentin
  13:00-13:30 EDT Hands-on, Quentin
Please download and install our VM
  https://github.com/qdeconinck/sigcomm20_mptp_tutorial
  And use slack channel for questions

## Slide 2: Multipath TCP
Olivier Bonaventure
https://inl.info.ucl.ac.be
https://perso.uclouvain.be/olivier.bonaventure
Thanks to Sébastien Barré, Christoph Paasch, Grégory Detal, Mark Handley, Costin Raiciu, Alan Ford, Micchio Honda, Fabien Duchene, Quentin De Coninck, Benjamin Hesmans, Viet-Hoang Tran and many others
SIGCOMM’20 Tutorial
The VM prepared by Quentin De Coninck for the hands-on is available from https://github.com/qdeconinck/sigcomm20_mptp_tutorial

## Slide 3: Agenda
Why Multipath TCP ?
Barriers to Multipath TCP
A closer look at the Multipath TCP protocol

## Slide 4: The Unix pipe model
echo
wc
1234 abbsbbbs

## Slide 5: The TCP bytestream model
Client
Server
ABCDEF...111232
0988989 ... XYZZ
IP:1.2.3.4
IP:4.5.6.7

## Slide 6: Endhosts have evolved
Mobile devices have multiple wireless interfaces and those using a single interface often support IPv4 and IPv6

## Slide 7: Two main types of use cases
Seamless handovers on smartphones
  With Multipath TCP, connections persit on smartphones even when they move from Wi-Fi to cellular and back
Bandwidth aggregation
  With Multipath TCP, heterogeneous networks can be combined to obtain higher bandwidth

## Slide 8: Multipath TCP use cases Low latency for Siri
Long-lived TLS connections
WiFi
3G/LTE
Voice samples
Voice samples

## Slide 9: Walking with Siri in 2012
xG celltower
Voice samples
Wi-Fi still attached but flappy
Wi-Fi lost, attach to cellular
Siri uses long-lived TLS connections
IP 1.2.3.4
IP 5.6.7.8
Restart TCP connection and send voice again…
Notes: ajouter adresse ip

## Slide 10: Walking with Siri and Multipath TCP
xG celltower
Voice samples
Wi-Fi still attached but flappy
Wi-Fi lost
Same applies to Apple Music and Apple Maps
IP 1.2.3.4
IP 5.6.7.8
Multipath TCP connection continues over cellular
Multipath TCP enables retransmission on cellular
Cellular available as backup
Notes: ajouter adresse ip

## Slide 11: Limitations of this use case today
Multipath TCP needed on smartphone+server
  Smartphone support for Multipath TCP
    Apple iOS since 2013, initially for Siri only and later for third-party applications and also Maps and Music
    Android, not part of the official release (Linux kernel)
      Samsung, LG, Huawei use it in specific markets
  Server support
    Well tested Linux patch https://www.multipath-tcp.org
    Ongoing work to bring it to mainline Linux kernel
  Load balancers
  Duchene, F., & Bonaventure, O. (2017, October). Making Multipath TCP friendlier to load balancers and anycast. In 2017 IEEE 25th International Conference on Network Protocols (ICNP) (pp. 1-10). IEEE.

## Slide 12: Multipath TCP use cases High bandwidth on smartphones
Koreans want 800+ Mbps on smartphones
WiFi
4G/LTE
Multipath TCP
Regular TCP
SOCKS
MPTCP<->TCP Proxy
Bonaventure, O., and Seo, S.. "Multipath TCP deployments." IETF Journal 12.2 (2016): 24-27.

## Slide 13: 5G/Wi-Fi coexistence
Same approach as for hybrid access networks
WiFi
5G
Multipath TCP
Regular TCP
ATSSS: Access Traffic Steering, Switching and Splitting
MPTCP<->TCP Proxy
Bonaventure, O., Boucadair, M. et al. ”0-RTT Convert Protocol" RFC8803, 2020
https://tools.ietf.org/html/rfc8803

## Slide 14: Broadband in the USA
Source: https://blogs.microsoft.com/on-the-issues/2019/04/08/ its-time-for-a-new-approach-for-mapping-broadband-data-to-better-serve-americans/

## Slide 15: Fast broadband in rural areas Europe
Source: https://ec.europa.eu/digital-single-market/en/news/study-broadband-coverage-europe-2018

## Slide 16: Hybrid Access Networks
DSL
4G/LTE
Multipath TCP
Regular TCP
Hybrid Access
Gateway
MPTCP<->TCP Proxy
TCP
TCP
Keukeleire, N., et al. (2020). Increasing Broadband Reach with Hybrid Access Networks. IEEE Communications Standards Magazine, 4(1), 43-49.
TCP<->MPTCP Proxy

## Slide 17: Other use cases
Multipath TCP on servers
  Can load-balance over heterogeneous links
  Ongoing effort for MPTCP in mainline Linux kernel
Multipath TCP in datacenters
  Proposed in SIGCOMM’11 paper, but not yet deployed AFAIK
Multipath TCP on dual-stack hosts
  Performance of IPv4 and IPv6 paths often differ
  Multipath TCP would automatically select the best
If you know other deployments, let me know !
http://blog.multipath-tcp.org/blog/html/2018/12/01/multipath_tcp_a_retrospective.html

## Slide 18: Agenda
Why Multipath TCP ?
Barriers to Multipath TCP
A closer look at the Multipath TCP protocol

## Slide 19: The Internet architecture that we explain to our students
Physical
Datalink
Network
Transport
Application
O. Bonaventure, et al. Computer networking : Principles, Protocols and Practice, open ebook, https://www.computer-networking.info
Physical
Physical
Datalink
Physical
Datalink
Network

## Slide 20: A typical "academic" network
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Physical
Datalink
TCP

## Slide 21: The end-to-end principle
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Physical
Datalink
TCP

## Slide 22: In reality
  almost as many middleboxes as routers
  various types of middleboxes are deployed
Sherry, Justine, et al. "Making middleboxes someone else's problem: Network processing as a cloud service." Proceedings of the ACM SIGCOMM 2012 conference. ACM, 2012.
Honda, Michio, et al. "Is it still possible to extend TCP?" Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference. ACM, 2011.

## Slide 23: A middlebox zoo
http://www.cisco.com/web/about/ac50/ac47/2.html
Web Security Appliance
NAC Appliance
ACE XML Gateway
Streamer
VPN Concentrator
SSL Terminator
Cisco IOS Firewall
IP Telephony Router
PIX Firewall Right and Left
Voice Gateway
Content Engine
NAT

## Slide 24: TCP segments processed by a router
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
IP
TCP

## Slide 25: TCP segments processed by a NAT
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Notes: c

## Slide 26: How to model those middleboxes ?
In the official architecture, they do not exist
In reality...
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
TCP
Physical
Datalink
Network
Transport
Application

## Slide 27: TCP segments processed by an ALG running on a NAT
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options

## Slide 28: How transparent is the Internet ?
25th September 2010 to 30th April 2011
142 access networks
24 countries
Sent specific TCP segments from client to a server in Japan
Honda, Michio, et al. "Is it still possible to extend TCP?" Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference. ACM, 2011.

## Slide 29: End-to-end transparency today
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Middleboxes don't change
the Protocol field, but
many discard packets with an unknown Protocol field

## Slide 30: TCP segments processed by a NAT (2)
active mode ftp behind a NAT
220 ProFTPD 1.3.3d Server (BELNET FTPD Server) [193.190.67.15]
ftp_login: user `<null>' pass `<null>' host `ftp.belnet.be'
Name (ftp.belnet.be:obo): anonymous
---> USER anonymous
331 Anonymous login ok, send your complete email address as your password
Password:
---> PASS XXXX
---> PORT 192,168,0,7,195,120
200 PORT command successful
---> LIST
150 Opening ASCII mode data connection for file list
lrw-r--r-- 1 ftp ftp 6 Jun 1 2011 pub -> mirror
226 Transfer complete

## Slide 31: Agenda
Why Multipath TCP ?
Barriers to Multipath TCP
A closer look at the Multipath TCP protocol

## Slide 32: Design objectives
Multipath TCP is an evolution of TCP
Design objectives
  Support unmodified applications
  Work over today’s networks (IPv4 and IPv6)
  Works in all networks where regular TCP works

## Slide 33: TCP Connection establishment
Three-way handshake
SYN,seq=1234,Options
SYN+ACK,ack=1235,seq=5678,Options
ACK,seq=1235,ack=5679

## Slide 34: Data transfer
seq=1234,"abcd"
ACK,ack=1238,win=4
seq=1238,"efgh"
ACK,ack=1242,win=0

## Slide 35: Connection release
seq=1234,"abcd"
RST

## Slide 36: Connection release
seq=1234,"abcd"
ACK,ack=1239
FIN,ack=350
seq=345,"ijkl"
FIN, seq=1238
FIN,seq=349

## Slide 37: Identification of a TCP connection
  Four tuple
  IPsource
  IPdest
  Portsource
  Portdest
  All TCP segments contain the four tuple
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
IP
TCP

## Slide 38: The new bytestream model
38
Client
Server
ABCDEF...111232
0988989 ... XYZZ
IP:1.2.3.4
IP:4.5.6.7
IP:2.3.4.5
IP:6.7.8.9
B
C
D
A
Notes: arrive fort tard

## Slide 39: The Multipath TCP protocol
Control plane
  How to manage a Multipath TCP connection that uses several paths ?
Data plane
  How to transport data ?
Congestion control
  How to control congestion over multiple paths ?

## Slide 40: A naïve Multipath TCP
SYN+ACK+Option
ACK
seq=123, "abc"
seq=126, "def"
SYN+Option

## Slide 41: A naïve Multipath TCP In today's Internet ?
SYN+Option
SYN+ACK+Option
ACK
seq=123, "abc"
seq=126, "def"
There is no corresponding TCP connection

## Slide 42: Design decision
  A Multipath TCP connection is composed of one or more regular TCP subflows that are combined
    Each host maintains state that glues the TCP subflows that compose a Multipath TCP connection together
    Each TCP subflow is sent over a single path and appears like a regular TCP connection along this path

## Slide 43: Multipath TCP and the architecture
Physical
Datalink
Network
Transport
Application
Multipath TCP
TCP1
socket
TCP2
TCPn
...
Application
A. Ford, C. Raiciu, M. Handley, S. Barre, and J. Iyengar, “Architectural guidelines for multipath TCP development", RFC6182 2011.
IPv4
IPv6

## Slide 44: A regular TCP connection
What is a regular TCP connection ?
  It starts with a three-way handshake
    SYN segments may contain special options
  All data segments are sent in sequence
    There is no gap in the sequence numbers
  It is terminated by using FIN or RST

## Slide 45: Multipath TCP
SYN+MP_CAPABLE
SYN+ACK+MP_CAPABLE
ACK+MP_CAPABLE
SYN+MP_JOIN
SYN+ACK+MP_JOIN
ACK

## Slide 46: How to combine two TCP subflows ?
SYN+MP_CAPABLE
SYN+ACK+ MP_CAPABLE
ACK+MP_CAPABLE
SYN+MP_JOIN
SYN+ACK+MP_JOIN
ACK
How to link with
blue subflow ?

## Slide 47: How to link TCP subflows ?
SYN, Portsrc=1234,Portdst=80+MP_CAPABLE
SYN+ACK[...]
ACK
SYN, Portsrc=1235,Portdst=80
+MP_JOIN[link Portsrc=1234,Portdst=80]
A NAT could change addresses and port numbers

## Slide 48: How to link TCP subflows ?
SYN, Portsrc=1234,Portdst=80 +MP_CAPABLE
SYN+ACK+MP_CAPABLE[Token=6543]
ACK+MP_CAPABLE [Token=5678]
SYN, Portsrc=1235,Portdst=80
+MP_JOIN[Token=6543]
MyToken=5678
YourToken=6543
MyToken=6543
YourToken=5678

## Slide 49: TCP subflows
Which subflows can be associated to a Multipath TCP connection ?
  At least one of the elements of the four-tuple needs to differ between two subflows
    Local IP address
    Remote IP address
    Local port
    Remote port

## Slide 50: Subflow agility
Multipath TCP supports
  addition of subflows
  removal of subflows

## Slide 51: The Multipath TCP protocol
Control plane
  How to manage a Multipath TCP connection that uses several paths ?
Data plane
  How to transport data ?
Congestion control
  How to control congestion over multiple paths ?

## Slide 52: How to transfer data ?
seq=123,"a"
seq=124,"b"
seq=125,"c"
seq=126,"d"
ack=124
ack=126
ack=125
ack=127

## Slide 53: How to transfer data in today's Internet ?
seq=123,"a"
seq=124,"b"
seq=125,"c"
ack=124
ack=126
ack=125
Gap in sequence numbering space
Some DPI will not allow this !

## Slide 54: Multipath TCP Data transfer
Two levels of sequence numbers
Multipath TCP
TCP1
socket
TCP2
Multipath TCP
TCP1
socket
TCP2
ABCDEF
Data sequence #
TCP1 sequence #
TCP2 sequence #

## Slide 55: Multipath TCP Data transfer
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DSeq=2, seq=124,"c"
DAck=1,ack=124
DAck=3, ack=125
DAck=2,ack=457

## Slide 56: Multipath TCP How to deal with losses ?
Data losses over one TCP subflow
  Fast retransmit and timeout as in regular TCP
Dseq=0,seq=123,"a"
DAck=1,ack=124
Dseq=0,seq=123,"a"
DAck=1,ack=124

## Slide 57: Multipath TCP
What happens when a TCP subflow fails ?
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=0,ack=457
Dseq=0,seq=457,"a"
DAck=2,ack=458

## Slide 58: Retransmission heuristics
Heuristics used by current Linux implementation
  Fast retransmit is performed on the same subflow as the original transmission
  Upon timeout expiration, reevaluate whether the segment could be retransmitted over another subflow
  Upon loss of a subflow, all the unacknowledged data are retransmitted on other subflows

## Slide 59: Flow control
How should the window-based flow control be performed ?
  Independant windows on each TCP subflow
  A single window that is shared among all TCP subflows

## Slide 60: Independant windows
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=100
Dseq=2,seq=457,"c"
DAck=3,ack=458,win=100
DAck=1,ack=124,win=0

## Slide 61: Independant windows possible problem
Impossible to retransmit, window is already full on green subflow
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=0

## Slide 62: A single window shared by all subflows
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DAck=2,ack=457,win=10
Dseq=2,seq=457,"c"
DAck=3,ack=458,win=10
DAck=1,ack=124,win=10

## Slide 63: Multipath TCP Windows
Multipath TCP maintains one window per Multipath TCP connection
  Window is relative to the last acked data (Data Ack)
  Window is shared among all subflows
    It's up to the implementation to decide how the window is shared
  Window is transmitted inside the window field of the regular TCP header
  If middleboxes change window field,
    use largest window received at MPTCP-level
    use received window over each subflow to cope with the flow control imposed by the middlebox

## Slide 64: Multipath TCP buffers
Multipath TCP
TCP1
socket
TCP2
Scheduler
Transmit queues, process only regular TCP header
Reorder queue, processes only TCP header
MPTCP-level, resequencing possible
send(...)
recv(...)

## Slide 65: Multipath TCP Data sequence numbers
What should be the length of the data sequence numbers ?
  32 bits
    compact and compatible with TCP
    wrap around problem at highspeed requires PAWS
  64 bits
    wrap around is not an issue anymore
    takes more space inside each segment

## Slide 66: Multipath TCP Data sequence numbers
Data sequence numbers and Data acknowledgements
  Maintained inside implementation as 64 bits field
  Implementations can, as an optimisation, only transmit the lower 32 bits of the data sequence and acknowledgements

## Slide 67: Other types of middlebox interference
Your favorite high-speed NIC
  GRO: Consecutive TCP segments can be merged
  TSO: A large TCP segment will be split in segments
  DSS is a mapping from DataSeq to SeqNum for a specific number of bytes
Application Level Gateway “modifies” payload
  Adding/Removing bytes is a problem
  DSS includes optional checksum to detect this and reset affected subflow or fallback TCP

## Slide 68: Multipath TCP option
A single option type
  to minimise the risk of having one option accepted by middleboxes in SYN segments and rejected in segments carrying data
Subtype
Kind Length
Subtype specific data
(variable length)

## Slide 69: Data Sequence Signal option
Cumulative Data ack
A = Data ACK present
a = Data ACK is 8 octets
M = mapping present
m = DSN is 8
Length of mapping, can extend beyond this segment
Computed over data covered by entire mapping + pseudo header

## Slide 70: The Multipath TCP protocol
Control plane
  How to manage a Multipath TCP connection that uses several paths ?
Data plane
  How to transport data ?
Congestion control
  How to control congestion over multiple paths ?

## Slide 71: TCP congestion control
A linear rate adaption algorithm
To be fair and efficient, a linear algorithm must use additive increase and multiplicative decrease (AIMD)
# Additive Increase Multiplicative Decrease
if congestion :
rate=rate*betaC # multiplicative decrease, betaC<1
else
rate=rate+alphaN # additive increase, v0>0

## Slide 72: AIMD in TCP
Congestion control mechanism
  Each host maintains a congestion window (cwnd)
  No congestion
    Congestion avoidance (additive increase)
      increase cwnd by one segment every round-trip-time
  Congestion
    TCP detects congestion by detecting losses
    Mild congestion (fast retransmit – multiplicative decrease)
      cwnd=cwnd/2 and restart congestion avoidance
    Severe congestion (timeout)
      cwnd=1, set slow-start-threshold and restart slow-start

## Slide 73: Congestion control for Multipath TCP
Simple approach
  independant congestion windows
Threshold
Threshold
Threshold

## Slide 74: Independent congestion windows
Problem
12Mbps

## Slide 75: Coupled congestion control
Congestion windows are coupled
  congestion window growth cannot be faster than TCP with a single flow
  Coupled congestion control aims at moving traffic away from congested path

## Slide 76: Linked increases congestion control
Algorithm
  Multiplicative Decrease
    For each loss on path r, cwinr=cwinr/2
  Additive increase
D. Wischik, C. Raiciu, A. Greenhalgh, and M. Handley, “Design, implementation and evaluation of congestion control for multipath TCP,” NSDI'11: Proceedings of the 8th USENIX conference on Networked systems design and implementation, 2011.

## Slide 77: Other Multipath-aware congestion control schemes
Y. Cao, X. Mingwei, and X. Fu, “Delay-based Congestion Control for Multipath TCP,” ICNP2012, 2012.
T. A. Le, C. S. Hong, and E.-N. Huh, “Coordinated TCP Westwood congestion control for multiple paths over wireless networks,” ICOIN '12: Proceedings of the The International Conference on Information Network 2012, 2012, pp. 92–96.
T. A. Le, H. Rim, and C. S. Hong, “A Multipath Cubic TCP Congestion Control with Multipath Fast Recovery over High Bandwidth-Delay Product Networks,” IEICE Transactions, 2012.
R. Khalili, N. Gast, M. Popovic, U. Upadhyay, J.-Y. Le Boudec , MPTCP is not Pareto-optimal: Performance issues and a possible solution, Proc. ACM Conext 2012
T. Dreibholz, M. Becke, J. Pulinthanath, and E. P. Rathgeb, “Applying TCP-Friendly Congestion Control to Concurrent Multipath Transfer,” Advanced Information Networking and Applications (AINA), 2010 24th IEEE International Conference on, 2010, pp. 312–319.

## Slide 78: Multipath TCP packet schedulers
When several subflows are active, the packet scheduler selects the subflow where each packet is sent
  Default scheduler is to prefer subflow having the lowest round-trip-time
    Well adapted to NewReno like congestion control
  Other schedulers have been proposed
    Round Robin, Priority
    Schedulers that schedule packets by estimating the time required to reach the receiver to avoid reodering
https://tools.ietf.org/html/draft-bonaventure-iccrg-schedulers

## Slide 79: The Multipath TCP protocol
Control plane
  How to manage a Multipath TCP connection that uses several paths ?
Data plane
  How to transport data ?
Congestion control
  How to control congestion over multiple paths ?

## Slide 80: Multipath TCP Connection establishment
Principle
SYN+ACK, MP_CAPABLE
ACK, MP_CAPABLE
seq=123, DSeq=1, "abc"
SYN, MP_CAPABLE
SYN+MP_JOIN
How to verify that
SYN+MP_JOIN comes from client of blue subflow ?

## Slide 81: Roles of the initial TCP handshake
Check willingness to open TCP connection
  Propose initial sequence number
  Negotiate Maximum Segment Size
TCP options
  negotiate Timestamps, SACK, Window scale
Multipath TCP
  check that server supports Multipath TCP
  propose Token in each direction
  propose initial Data sequence number in each direction
  Exchange keys to authenticate subflows

## Slide 82: « Authenticating » Multipath TCP subflows
Main goal
  Prevent attacks by off-path attackers
Principles
  Each host announces a key during initial handshake
    keys are exchanged in clear
  When establishing a subflow, use HMAC + key to authenticate subflow

## Slide 83: Key exchange
SYN+ACK, MPC[MyKey="keyDEF"]
ACK MPC[MyKey="keyABC", YourKey="keyDEF"]
SYN, MPC
SYN,MP_JOIN[NonceA=123]
SYN+ACK[NonceB=456, HMAC(123||456,"keyDEF||keyABC")]
ACK,[HMAC(456||123,"keyABC||keyDEF")]
MyKey="keyABC"
YourKey="keyDEF"
MyKey="keyDEF"
YourKey="keyABC"

## Slide 84: The MP_CAPABLE option
A: DSN Checksum
required or not
Load balancers
Used inside SYN+ACK
In SYN+ACK and third ACK

## Slide 85: Initial Data Sequence Numbers and Tokens
Computation of initial Data Sequence Number
Computation of token
TokenA=Upper32(SHA-1(KeyA))
TokenB=Upper32(SHA-1(KeyB))
IDSNA=Lower64(SHA-1(KeyA))
IDSNB=Lower64(SHA-1(KeyB))
There is a small risk of collision,
different keys
same token

## Slide 86: The Multipath TCP control plane
Connection establishment in details
Closing a Multipath TCP connection
Address dynamics

## Slide 87: Closing a Multipath TCP connection
seq=123, DSS[1->123 ...], "ab"
DAck=9,ack=128
seq=456, DSS[3->456], "cd"
DAck=5,ack=458
seq=125, DSS[5->125,DATA_FIN ...], "end"
seq=128, FIN
ack=129

## Slide 88: Quickly closing a Multipath TCP connection
RST
RST
How to quickly close a Multipath TCP connection ?
  By closing all subflows ?

## Slide 89: Closing a Multipath TCP connection
FAST Close
SYN+ACK, [...]
ACK[...]
SYN,[...]
SYN+ACK[...]
ACK[..]
SYN, [...]
ACK+FAST_CLOSE(ClientKey)
RST
RST

## Slide 90: The Multipath TCP control plane
Connection establishment in details
Closing a Multipath TCP connection
Address dynamics

## Slide 91: Multipath TCP Address dynamics
How to learn the addresses of a host ?
How to deal with address changes ?
IP=1.2.3.4
IP=4.5.6.7
IP=2.3.4.5
IP=3.4.5.6
IP6=2a00:1450:400c:c05::69

## Slide 92: Address dynamics
Basic solution : multihomed server
IP=2.3.4.5
IP=3.4.5.6
IP6=2a00:1450:400c:c05::69
SYN+ACK, [...]
ACK[...]
SYN, [...]
ADD_ADDR[3.4.5.6]
ADD_ADDR[2a00:1450:400c:c05::69]
SYN,[...]
SYN+ACK[...]
ACK[..]

## Slide 93: Address dynamics
Basic solution : mobile client
IP=2.3.4.5
SYN+ACK, [...]
ACK[...]
SYN, [...]
IP=1.2.3.4
IP=4.5.6.7
ADD_ADDR [4.5.6.7]
SYN,[...]
SYN+ACK[...]
ACK[..]
REMOVE_ADDR[1.2.3.4]

## Slide 94: Address dynamics in today's Internet
IP=2.3.4.5
SYN+ACK, [...]
ACK[...]
SYN, [...]
IP=1.2.3.4
IP=10.0.0.2
ADD_ADDR [10.0.0.2]
SYN [...]
ADD_ADDR [10.0.0.2]
?
NAT

## Slide 95: Address dynamics with NATs
Solution
  Each address has one identifier
    Subflow is established between id=0 addresses
  Each host maintains a list of <address,id> pairs of the addresses associated to an MPTCP endpoint
  MPTCP options refer to the address identifier
    ADD_ADDR contains <address,id>
    REMOVE_ADDR contains <id>

## Slide 96: Address dynamics
IP=2.3.4.5
SYN+ACK, [...]
ACK[...]
SYN, [...]
IP=1.2.3.4
IP=4.5.6.7
ADD_ADDR [4.5.6.7,id=1]
SYN,[id=1...]
SYN+ACK[...]
ACK[..]
REMOVE_ADDR[id=0]

## Slide 97: The Multipath TCP Path Manager
Leverages the information about
  Local IP addresses and interface state
  Remote IP addresses
Decides to create and terminate subflows
Sample path managers
  Full mesh : one subflow between each pair addr.
  Ndiffports: for single-homed hosts, n parallel flows
  Use case specific path managers

## Slide 98: Multipath TCP aware load-balancers
IP=2.3.4.5
IP=1.2.3.4
SYN+ACK, MPC[C=1,...]
ACK MPC[...]
SYN, MPC
ADD_ADDR[3.4.5.6]
SYN,[...]
ACK[..]
IP=3.4.5.6
IP=3.4.5.7
SYN, MPC
ACK[...]
SYN+ACK[...]
  Duchene, F., & Bonaventure, O. (2017, October). Making Multipath TCP friendlier to load balancers and anycast. In 2017 IEEE 25th International Conference on Network Protocols (ICNP) (pp. 1-10). IEEE.

## Slide 99: Conclusion
Multipath TCP is a reality
  Many scientific papers (see references)
  Due to the middleboxes, the protocol is more complex than initially expected
  Multipath TCP works over today's Internet !
    Large scale deployments
What's next ?
  Ongoing effort to integrate it in the mainline Linux kernel for wider deployment

## Slide 100: Hands-on
First check that the VM is working correctly
https://github.com/qdeconinck/sigcomm20_mptp_tutorial

## Slide 101: Hands-on : bandwidth aggregation

## Slide 102: Comparing packet schedulers

## Slide 103: Comparing packet schedulers (2)

## Slide 104: Path managers

## Slide 105: Try it by yourself ! https://multipath-tcp.org

## Slide 106: References
The Multipath TCP protocol
  https://www.multipath-tcp.org
  http://tools.ietf.org/wg/mptcp/
A. Ford, C. Raiciu, M. Handley, S. Barre, and J. Iyengar, “Architectural guidelines for Multipath TCP development", RFC6182 2011.
C. Raiciu, C. Paasch, S. Barre, A. Ford, M. Honda, F. Duchene, O. Bonaventure, and M. Handley, “How hard can it be? designing and implementing a deployable multipath TCP,” NSDI'12: Proceedings of the 9th USENIX conference on Networked Systems Design and Implementation, 2012.
A. Ford, C. Raiciu, M. J. Handley, and O. Bonaventure, “TCP Extensions for Multipath Operation with Multiple Addresses,” RFC6824, 2013
A. Ford, C. Raiciu, M. J. Handley, and O. Bonaventure, C. Paasch, “TCP Extensions for Multipath Operation with Multiple Addresses,” RFC8684, 2020

## Slide 107: Multipath TCP : RFCs
RFC6181: Threat Analysis for TCP Extensions for Multipath Operation with Multiple Addresses
RFC6182: Architectural Guidelines for Multipath TCP Development
RFC6356: Coupled Congestion Control for Multipath Transport Protocols
RFC6824: TCP Extensions for Multipath Operation with Multiple Addresses (v0)
RFC6897: Multipath TCP (MPTCP) Application Interface Considerations
RFC7430: Analysis of Residual Threats and Possible Fixes for Multipath TCP (MPTCP)
RFC8041: Use Cases and Operational Experience with Multipath TCP
RFC8684: TCP Extensions for Multipath Operation with Multiple Addresses (v1)

## Slide 108: Implementations
Linux
  Patches to different kernel versions supporting v0
    http://www.multipath-tcp.org
    https://github.com/multipath-tcp
  Ongoing effort by RedHat, Apple, intel and Tessares to include Multipath TCP v1 in mainline Linux
    https://github.com/multipath-tcp/mptcp_net-next/wiki
Apple
  Included in iOS and MacOS
FreeBSD (not updated)
  http://caia.swin.edu.au/urp/newtcp/mptcp/

## Slide 109: Multipath TCP tutorials and surveys
  Paasch, C., & Bonaventure, O. (2014). Multipath tcp. Communications of the ACM, 57(4), 51-57.
  Raiciu, C., Iyengar, J., & Bonaventure, O. (2013). Recent advances in reliable transport protocols. SIGCOMM ebook on Recent Advances in Networking.
  Bonaventure, O., Handley, M., & Raiciu, C. (2012). An overview of Multipath TCP. ; login:, 37(5), 17.
  Li, M., Lukyanenko, A., Ou, Z., Ylä-Jääski, A., Tarkoma, S., Coudron, M., & Secci, S. (2016). Multipath transmission for the internet: A survey. IEEE Communications Surveys & Tutorials, 18(4), 2887-2925.
  Polese, M., Chiariotti, F., Bonetto, E., Rigotto, F., Zanella, A., & Zorzi, M. (2019). A survey on recent advances in transport layer protocols. IEEE Communications Surveys & Tutorials, 21(4), 3584-3608.

## Slide 110: Use cases
  Bonaventure, O., & Seo, S. (2016). Multipath TCP deployments. IETF Journal, 12(2), 24-27.
  C. Paasch, G. Detal, F. Duchene, C. Raiciu, and O. Bonaventure, “Exploring mobile/WiFi handover with multipath TCP,” CellNet '12: Proceedings of the 2012 ACM SIGCOMM workshop on Cellular networks: operations, challenges, and future design, 2012.
  De Coninck, Q., Baerts, M., Hesmans, B., & Bonaventure, O. (2016). Observing real smartphone applications over multipath TCP. IEEE Communications Magazine, 54(3), 88-93.
  Nikravesh, A., Guo, Y., Qian, F., Mao, Z. M., & Sen, S. (2016, October). An in-depth understanding of multipath TCP on mobile devices: Measurement and system design. In Proceedings of the 22nd Annual International Conference on Mobile Computing and Networking (pp. 189-201).
  C. Raiciu, S. Barre, C. Pluntke, A. Greenhalgh, D. Wischik, and M. J. Handley, “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.
  Duchene, F., & Bonaventure, O. (2017, October). Making multipath tcp friendlier to load balancers and anycast. In 2017 IEEE 25th International Conference on Network Protocols (ICNP) (pp. 1-10). IEEE.
  Keukeleire, N., Hesmans, B., & Bonaventure, O. (2020). Increasing Broadband Reach with Hybrid Access Networks. IEEE Communications Standards Magazine, 4(1), 43-49.

## Slide 111: Middleboxes and Multipath TCP
M. Honda, Y. Nishida, C. Raiciu, A. Greenhalgh, M. Handley, and H. Tokuda, “Is it still possible to extend TCP?,” IMC '11: Proceedings of the 2011 ACM SIGCOMM conference on Internet measurement conference, 2011.
Detal, G., Hesmans, B., Bonaventure, O., Vanaubel, Y., & Donnet, B. (2013, October). Revealing middlebox interference with tracebox. In Proceedings of the 2013 conference on Internet measurement conference (pp. 1-8).
Hesmans, B., Duchene, F., Paasch, C., Detal, G., & Bonaventure, O. (2013, December). Are TCP extensions middlebox-proof?. In Proceedings of the 2013 workshop on Hot topics in middleboxes and network function virtualization (pp. 37-42).

## Slide 112: Multipath congestion control
  Background
  Coupled congestion control
D. Wischik, C. Raiciu, A. Greenhalgh, and M. Handley, “Design, implementation and evaluation of congestion control for multipath TCP,” NSDI'11: Proceedings of the 8th USENIX conference on Networked systems design and implementation, 2011.
C. Raiciu, M. J. Handley, and D. Wischik, “Coupled Congestion Control for Multipath Transport Protocols,” RFC, vol. 6356, Oct. 2011.
D. Wischik, M. Handley, and M. B. Braun, “The resource pooling principle,” ACM SIGCOMM Computer …, vol. 38, no. 5, 2008.
P. Key, L. Massoulie, and P. D. Towsley, “Path Selection and Multipath Congestion Control,” INFOCOM 2007. 2007, pp. 143–151.
F. Kelly and T. Voice. Stability of end-to-end algorithms for joint routing and rate control. ACM SIGCOMM CCR, 35, 2005.

## Slide 113: Multipath congestion control
Y. Cao, X. Mingwei, and X. Fu, “Delay-based Congestion Control for Multipath TCP,” ICNP2012, 2012.
T. A. Le, C. S. Hong, and E.-N. Huh, “Coordinated TCP Westwood congestion control for multiple paths over wireless networks,” ICOIN '12: Proceedings of the The International Conference on Information Network 2012, 2012, pp. 92–96.
T. A. Le, H. Rim, and C. S. Hong, “A Multipath Cubic TCP Congestion Control with Multipath Fast Recovery over High Bandwidth-Delay Product Networks,” IEICE Transactions, 2012.
R. Khalili, N. Gast, M. Popovic, U. Upadhyay, J.-Y. Le Boudec , MPTCP is not Pareto-optimal: Performance issues and a possible solution, Proc. ACM Conext 2012
T. Dreibholz, M. Becke, J. Pulinthanath, and E. P. Rathgeb, “Applying TCP-Friendly Congestion Control to Concurrent Multipath Transfer,” Advanced Information Networking and Applications (AINA), 2010 24th IEEE International Conference on, 2010, pp. 312–319.

## Slide 114: Multipath TCP : schedulers
  Paasch, C., Ferlin, S., Alay, O., & Bonaventure, O. (2014, August). Experimental evaluation of multipath TCP schedulers. In Proceedings of the 2014 ACM SIGCOMM workshop on Capacity sharing workshop (pp. 27-32).
  Frömmgen, A., Rizk, A., Erbshäußer, T., Weller, M., Koldehofe, B., Buchmann, A., & Steinmetz, R. (2017, December). A programming model for application-defined multipath TCP scheduling. In Proceedings of the 18th ACM/IFIP/USENIX Middleware Conference (pp. 134-146).
  De Coninck, Q., & Bonaventure, O. (2018, May). Tuning multipath TCP for interactive applications on smartphones. In 2018 IFIP Networking Conference (IFIP Networking) and Workshops (pp. 1-9). IEEE.
  Ferlin, S., Alay, Ö., Mehani, O., & Boreli, R. (2016, May). BLEST: Blocking estimation-based MPTCP scheduler for heterogeneous networks. In 2016 IFIP Networking Conference (IFIP Networking) and Workshops (pp. 431-439). IEEE.
  Corbillon, X., Aparicio-Pardo, R., Kuhn, N., Texier, G., & Simon, G. (2016, May). Cross-layer scheduler for video streaming over MPTCP. In Proceedings of the 7th International Conference on Multimedia Systems (pp. 1-12).
  O. Bonaventure, M. Piraux, M. Baerts, C. Paasch, M. Amend, Multipath schedulers, draft-bonaventure-iccrg-schedulers-00, 2020

## Slide 115: Multipath TCP : Path management
  Hesmans, B., Detal, G., Barre, S., Bauduin, R., & Bonaventure, O. (2015, December). Smapp: Towards smart multipath tcp-enabled applications. In Proceedings of the 11th acm conference on emerging networking experiments and technologies (pp. 1-7).
  Hesmans, B., & Bonaventure, O. (2016, July). An enhanced socket API for Multipath TCP. In Proceedings of the 2016 applied networking research workshop (pp. 1-6).
  Othman, O. & Martineau, M. The Multipath TCP Daemon, https://github.com/intel/mptcpd
  Tran, V.-H., Bonaventure, O., Beyond socket options: Towards fully extensible Linux transport stacks. In Computer Communications, 2020